## Slide 1: THESIS –II Name: Sofeem Nasim Roll No: L11-5255 Supervisor :- Dr. Kashif Zafar
Layout Optimization for a Wireless Sensor Network using Multi-Objective Firefly Algorithm

## Slide 2: Outline
Introduction
Problem Statement
Literature View
Proposed Solution
Implementation
Experiment and Results
Conclusion
Future Work

## Slide 3: Introduction

## Slide 4: Wireless Network Sensor
Wireless sensor network is a collection of spatial distribution autonomous sensor. Collectively work together to monitor physical or environment (such as temperature, sound, pressure etc.). Provide simple transmission to the Data processing Unit (Base Station.) [1]

## Slide 5: Sensor and its Types
  Sensing + Processing + Communication
Generally three kinds of nodes.
  Senor Node: Measure physical quantities.
  Relay Node: Transmit data to sink node.
  Sink Node: High Energy Communication. []

## Slide 7: Sensor Limitations
Limited computation capacity
Limited memory
Limited power resource
Short radio communication device

## Slide 8: Applications of WSNs
Constant monitoring & detection of specific events
Military, battlefield surveillance
Forest fire & flood detection
Habitat exploration of animals
Patient monitoring
Home appliances

## Slide 9: Challenges
Coverage problem:
Coverage problem is termed as the problem of positioning the sensor in such a way such that the network attains maximum percentage of coverage in region of interest by using N sensors. []

## Slide 10
Network Lifetime :
It is defined as the time until the network gets partitioned in a way that is impossible to collect the data from a part of the network. []

## Slide 11: Problem Statement
Maximizing network parameters like coverage lifetime etc. is one of the most important task in designing the layout for wireless sensor network.
Random positioning of sensor node can leads to poor coverage and indelicate lifetime of the network in the real environment.
On the other hand network parameters like coverage, cost and network lifetime are contradictory which poses a challenge to the design of layout

## Slide 12
Literature Review

## Slide 13: A Survey of Multi-Objective Deployment in Wireless Sensor Networks[]
The paper examines the deployment of sensor with respect to WSN applications.
Highlights the main properties and criteria to determine that how should sensor be deployed according to WSN application.
Provides an overview of multi-objective strategies

## Slide 14: Layout Optimization for a Wireless Sensor Network Using a Multi-Objective Genetic Algorithm[]
MOGA is used to optimize layout of wireless sensor network keeping two objective coverage and lifetime under consideration.
The important point in the paper is to show that GA can help to provide good layout even when we are dealing with multi-objective optimization problem.
The proposed solution have slow convergence due to GA.

## Slide 15: A Wireless Sensor Network Coverage Optimization Algorithm Based on Particle Swarm Optimization and Voronoi Diagram []
This paper proposes a new algorithm to optimize sensor coverage using particle swarm optimization (PSO) and Voronoi diagram.
PSO is used to find the optimal deployment of the sensors that gives the best coverage
Voronoi diagram is used to evaluate the fitness of the solution.
The proposed solution is only focused on maximization of coverage

## Slide 16: Energy Efficient Layout for a Wireless Sensor Network using Multi-Objective Particle Swarm Optimization []
The paper focus is on energy efficient layout optimization of wireless sensor network
Multi-objective particle swarm Optimization algorithm is proposed to optimize two objective coverage and lifetime.
Faster convergence as compared to MOGA
The proposed solution does not explore complete search space and results in premature convergence .

## Slide 17: Fire-Fly Algorithm
Firefly newly developed meta-heuristic algorithm introduced by Xin-She Yang in 2008, inspired by the flashing pattern and behavior of fireflies
. Three characteristic of Fire fly:
  Firefly attract each other through their flashing pattern
  The attractiveness is proportional to the brightness, and they both decrease as their distance increases.
  The brightness of a firefly is determined by the landscape of the objective function.

## Slide 18: FireFly
Each firefly contains complete solution.
Brightness of each firefly is associated with the value of objective function.
Light intensity of firefly is determined by its brightness.
Each firefly attract another through its light intensity.

## Slide 19: Formulation
Attractiveness:
β = βoe-γr2
Where ,
β is the firefly attractiveness coefficient.
γ is absorption coefficient

## Slide 20
Movement:
              xi t+1 = xit + βoe-γr2 + αεit
where , second term is associated with the attractiveness and Gamma is random factor

## Slide 21: Why Firefly is efficient ?
Firefly is swarm-intelligence-based algorithm has two benefits over other swarm-based algorithm
Two benefits:
    automatic subdivision
    deal with multimodality

## Slide 22: Proposed methodology

## Slide 23: Approach
Placement of Sensor is critical factor
Optimal placement of sensor nodes in an area can offer benefits like longer network lifetime, better coverage and connectivity
Many conflicting Factors (Coverage and Lifetime)

## Slide 24
A optimization technique( Multi-Objective FireFly Algorithm, MOFA) is used with this simplified model to provide end-user with a set of Pareto-optimal network designs with maximizing coverage and lifetime of the network.

## Slide 25: Multi-objective optimization
Multi-objective optimization:
  Considers two or more objectives, each having an objective function, one or more optimal solutions are found
  These optimal solutions are termed as Pareto Optimal Solutions
  Example:
    Buy a car with maximum comfort ability and minimum price
    Route planning with minimum cost of the route and maximum coverage of the cities between source and destination
Why considering multi-objective problem?
  Single objective – provides a single best solution to the problem
  Multi-objective – provides multiple best solutions to the problem

## Slide 26: Layout Optimization Using Multi-Objective FireFly Algorithm
In the proposed solution to two conflicting objectives are considered coverage and lifetime.
Multi-objective Firefly algorithm is used to optimize layout for WSN

## Slide 28: Modeling of Firefly
Firefly encoding representation:
Each firefly contains complete solutions. The design variable is (x,y) coordinates of the sensors in the area to be covered. Each firefly contains design variable of n sensors given as DV = {(x1,y1) ,(x2,y2)……(xn,yn)}.
Firefly representation:
Sensor1 (x1,y1) | Sensor2 (x2,y2) | Sensor3 (x3,y3) | ………………. | SensorN (xN,yN)

## Slide 29: Objective Function
Coverage
where Ai is the area covered by ith node, N total number of nodes deployed and A is total area that is in interest to be covered.

## Slide 30
Lifetime = mini…N (Tfailure , i )/Tmax
where Tfailure is maximum sensing cycle until the first node dies
Tmax is the total sensing cycle that network contains

## Slide 31
Solution Space
Firefly are randomly distributed in SS

## Slide 32
Update light Intensity of Each Firefly
Light intensity : 6
Light intensity : 6.9
Light intensity : 5.4
Light intensity : 8
Light intensity :7
Light intensity : 6
Light intensity : 6.4
Light intensity : 6.7
Light intensity : 2.5
Light intensity : 3

## Slide 33
Experiment and Results

## Slide 34: Experiment
Experiment is conducted in two parts
Finding best parameter setting of firefly algorithm.
Comparative analysis between firefly and PSO (with single objective). And finding pareto optimal solution using MOFA.

## Slide 35: Experiment Setup
Tool:-
The experiment is conducted in Java(Net-bean 7.1) to simulate wireless sensor network

## Slide 36: Experiment
In the following experiment the parameters are taken to simulate wireless sensor network are: grid size of 10X10, 10 sensors with 2m sensing radius

## Slide 37
Results

## Slide 38: Alpha as 0.1
beta | gamma | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9
0.1 |  | 76.2 | 78.6 | 79.2 | 79 | 79.8 | 79.2 | 76.8 | 75.4 | 77.8
0.2 |  | 76.6 | 78.4 | 78.8 | 79.2 | 79.2 | 78 | 76.4 | 78.4 | 78.6
0.3 |  | 77 | 77.4 | 77.4 | 78.4 | 76.6 | 77.6 | 76.8 | 74.8 | 77.2
0.4 |  | 79.2 | 78.2 | 77 | 78.4 | 78.8 | 79 | 80.8 | 76.2 | 79
0.5 |  | 78.8 | 77 | 77.4 | 77 | 77.2 | 76.2 | 77 | 75 | 79
0.6 |  | 77.6 | 77 | 75.2 | 76.4 | 79.4 | 78 | 78.4 | 75.4 | 79
0.7 |  | 77.8 | 77.8 | 78.8 | 79.6 | 78 | 76.4 | 79 | 77.2 | 78.2
0.8 |  | 78.2 | 77.4 | 79.2 | 82.2 | 78 | 78.6 | 75 | 78.6 | 77.4
0.9 |  | 76.2 | 80.4 | 80.6 | 81 | 80.4 | 80.2 | 77.4 | 78.2 | 83.2

## Slide 39: Alpha as 0.2
beta | gamma | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9
0.1 |  | 79.6 | 78.6 | 77.4 | 79.8 | 77.8 | 77.4 | 76.2 | 82 | 77.4
0.2 |  | 76.4 | 78 | 77.8 | 77.8 | 78.6 | 79.4 | 76.6 | 79.4 | 77.2
0.3 |  | 77 | 79.2 | 79.6 | 79.8 | 76.4 | 79 | 79.4 | 74.2 | 76.4
0.4 |  | 77.4 | 78.6 | 78 | 76.8 | 76 | 77.4 | 80.4 | 77.4 | 77.2
0.5 |  | 78.4 | 77.6 | 79.2 | 78 | 79.6 | 79 | 73.4 | 79.4 | 78.6
0.6 |  | 78.4 | 79.8 | 79.8 | 79.4 | 77.8 | 78.4 | 78.6 | 77.2 | 76
0.7 |  | 80.2 | 77.8 | 78.6 | 80 | 77.8 | 76.4 | 75.2 | 78.2 | 77.8
0.8 |  | 73.8 | 77.2 | 76.2 | 77.6 | 78.8 | 78.4 | 77.4 | 78.6 | 76.8
0.9 |  | 76.6 | 80 | 79.4 | 79.8 | 79 | 80.2 | 78.2 | 80.4 | 79.8

## Slide 40: Alpha as 0.3
beta | gamma | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9
0.1 |  | 79.6 | 78.4 | 78.4 | 80.4 | 77 | 76.6 | 79 | 77.6 | 78.4
0.2 |  | 76.4 | 79.2 | 79.2 | 79.4 | 76.4 | 79 | 78.6 | 77.8 | 76.2
0.3 |  | 77 | 80.8 | 80.8 | 80 | 76.8 | 77.8 | 78.6 | 79.8 | 77.4
0.4 |  | 77.4 | 78.8 | 78.8 | 78 | 78.4 | 80.6 | 77.2 | 75.2 | 77.8
0.5 |  | 77.2 | 75.8 | 75.8 | 76.4 | 77.8 | 78.6 | 77.6 | 75.4 | 80.8
0.6 |  | 75.8 | 76.4 | 76.4 | 78.2 | 78.4 | 77.6 | 78.4 | 77.6 | 77.6
0.7 |  | 76.6 | 76.8 | 76.8 | 77.2 | 78.4 | 80 | 78 | 79.2 | 76.2
0.8 |  | 79.6 | 79.4 | 79.4 | 77.2 | 77.8 | 79 | 76 | 77.2 | 76.4
0.9 |  | 79 | 76.8 | 76.8 | 79.2 | 80.6 | 81.6 | 79 | 78.6 | 79.6

## Slide 41: Alpha as 0.4
beta | gamma | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9
0.1 |  | 77.4 | 81 | 77.4 | 76.8 | 78.6 | 77.6 | 79.2 | 77.2 | 78.4
0.2 |  | 77.4 | 79.4 | 77.8 | 79.4 | 79.4 | 78.6 | 79 | 78.2 | 80
0.3 |  | 77.8 | 80.2 | 76.4 | 77.6 | 77.4 | 79.4 | 79 | 78.2 | 78.8
0.4 |  | 80.6 | 77.4 | 76.4 | 77.6 | 77.6 | 79.4 | 78.2 | 79.4 | 79.2
0.5 |  | 79.4 | 79.2 | 76.8 | 77.2 | 77.2 | 79.4 | 79 | 77.8 | 80
0.6 |  | 75.8 | 75.8 | 80 | 79 | 79 | 75.4 | 78.8 | 78 | 79
0.7 |  | 77.2 | 78 | 80 | 79 | 79 | 81 | 78.6 | 77.4 | 78
0.8 |  | 78.2 | 80 | 77 | 76.2 | 76.2 | 76.6 | 79.8 | 78.8 | 80
0.9 |  | 77.4 | 77.2 | 80.2 | 77.2 | 76 | 78.2 | 77.8 | 77 | 78.6

## Slide 42: Alpha as 0.5
beta | gamma | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9
0.1 |  | 79.2 | 78.6 | 80.6 | 79.2 | 78.4 | 81.2 | 76.6 | 78.4 | 79.2
0.2 |  | 77.2 | 78.6 | 77.4 | 78.8 | 78.2 | 78.8 | 80.8 | 77.8 | 76.8
0.3 |  | 76.4 | 78.4 | 78.8 | 79 | 78.6 | 80 | 75.8 | 79.4 | 77.8
0.4 |  | 78.4 | 80 | 78.8 | 79 | 76.8 | 77.8 | 77.2 | 79.2 | 80.2
0.5 |  | 77.3 | 78.4 | 78.4 | 78.2 | 79 | 81 | 79.4 | 77.5 | 78.8
0.6 |  | 77.4 | 78.4 | 77.4 | 78 | 79.6 | 78.8 | 78.8 | 80 | 76
0.7 |  | 79.8 | 77 | 77.4 | 77.2 | 78.2 | 77.2 | 75 | 80.2 | 79
0.8 |  | 77.44 | 79.4 | 74.3 | 77.2 | 78.2 | 76.8 | 77.2 | 78.6 | 77.8
0.9 |  | 79.4 | 79.6 | 79.6 | 77.8 | 77.4 | 79.6 | 81.2 | 78.6 | 80.4

## Slide 43: Alpha as 0.6
beta | gamma | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9
0.1 |  | 79.8 | 78 | 80.6 | 78.6 | 80.2 | 77.4 | 78.6 | 77.4 | 77.4
0.2 |  | 77.6 | 77.4 | 76.8 | 79.8 | 75.2 | 79.4 | 79 | 80.6 | 83.6
0.3 |  | 79.2 | 77.2 | 79.2 | 76.8 | 77.6 | 79 | 80.4 | 78 | 80
0.4 |  | 78 | 79.4 | 79 | 75.6 | 77 | 77.4 | 80.2 | 79.2 | 78.4
0.5 |  | 77 | 82.8 | 81.8 | 75.4 | 78.6 | 79 | 77 | 77.8 | 77.6
0.6 |  | 77.4 | 79.6 | 78.6 | 76 | 75.8 | 78.4 | 80.6 | 78.8 | 78.8
0.7 |  | 79.6 | 79.4 | 78.8 | 78.6 | 77.4 | 78.8 | 76.6 | 77 | 79.2
0.8 |  | 78.8 | 78.4 | 81.4 | 77.6 | 78 | 79.2 | 78.2 | 79.4 | 78.6
0.9 |  | 80.2 | 78.6 | 76.8 | 77.4 | 76.6 | 78.4 | 75.6 | 77.4 | 84.4

## Slide 44: Comparative Analysis of Firefly and PSO (with Single objective of Coverge)
In the second part two experiment are conducted to show that how firefly algorithm will present better results than PSO .
Experiment 1 setup :
Includes the layout of wireless sensor network in which grid size is 10X10 with sensing radius of sensor is 2 and the number of sensor includes in the simulation are 10.

## Slide 45: Results with Firefly
Firefly Algorithm | Iterations |  |  |  |  |  |  | 
 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80
# Firefly | Average of 5 Runs |  |  |  |  |  |  | 
5 | 90.3% | 90.1% | 90.1% | 90.2% | 90.8% | 91.5% | 91.7% | 92.2%
10 | 92.2% | 92.6% | 92.9% | 94% | 94.12% | 94.9% | 95.4% | 95.3%
15 | 94% | 92.2% | 91.1% | 92.2% | 92.4% | 93.13% | 92.9% | 94.74%
20 | 93.82% | 93.8% | 95.15% | 93.36% | 95.4% | 94.5% | 93.5% | 96.42%
25 | 91.5% | 94% | 97% | 91.7% | 95.15% | 93.5% | 93.8% | 92.9%

## Slide 46: Results with PSO
PSO Algorithm | Iterations |  |  |  |  |  |  | 
 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80
# Swarm | Average of 5 Runs |  |  |  |  |  |  | 
5 | 83.52% | 86.04% | 80.54% | 85.55% | 78.94% | 84.21% | 84.2% | 81.92%
10 | 86.95% | 90% | 83.9% | 84.89% | 84.21% | 89.99% | 88.55% | 87.64%
15 | 89.93% | 89.47% | 87.87% | 88.55% | 85.12% | 90.9% | 90.6% | 86.72%
20 | 90.16% | 87.87% | 87.41% | 90.38% | 89.24% | 91% | 88.55% | 89.93%
25 | 91% | 89.70% | 91.9% | 91.9% | 89.4% | 90.16% | 91% | 89.4%

## Slide 47: Analysis
As a result show that the firefly algorithm provides better coverage than the particle swarm optimization algorithm applying similar conditions of wireless sensor network. The firefly algorithm is providing 97% efficiency of coverage in designing the layout of WSN while particle swarm optimization is providing 91.9%.

## Slide 48
In the second experiment :
The context of experiment includes the layout of wireless sensor network in which grid size is 20X20 with sensing radius of sensor is 3 and the number of sensor includes in the simulation are 10

## Slide 49: Results of firefly
Firefly Algorithm | Iterations |  |  |  |  |  |  | 
 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80
# Firefly | Average of 5 Runs |  |  |  |  |  |  | 
5 | 88.92% | 86.61% | 88.02% | 88.48% | 87.23% | 87.67% | 91.08% | 91.89%
10 | 88.11% | 89.29% | 90.92% | 90.25% | 90.47% | 91.45% | 91.9% | 92.11%
15 | 91.88% | 91.88% | 91.51% | 93.57% | 92.54% | 91.80% | 92.84% | 91.73%
20 | 91.51% | 93.57% | 92.54% | 91.80% | 94.39% | 92.91% | 91.79% | 93.65%
25 | 92.38% | 92.53% | 91.66% | 92.91% | 93.13% | 93.21% | 94.02% | 94.46%

## Slide 50: Results of PSO
PSO Algorithm | Iterations |  |  |  |  |  |  | 
 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80
# Firefly | Average of 5 Runs |  |  |  |  |  |  | 
5 | 79% | 82% | 83.7% | 82.3% | 82.5S% | 82.9% | 82.40% | 80.33%
10 | 86.24% | 86.90% | 85.83% | 84.57% | 87.24% | 83.9% | 85.57% | 87.08%
15 | 85.84% | 85.5% | 83.98% | 87.24% | 85.84% | 87.73% | 86.19% | 85.48%
20 | 83.58% | 85.44% | 85.80% | 87.52% | 87.52% | 88.74% | 88.75% | 87.3%
25 | 86.83% | 85.72% | 85.75% | 88.3% | 87.86% | 89.22% | 88.22% | 88.63%

## Slide 51: Analysis
As a result show that the firefly algorithm provides better coverage than the particle swarm optimization algorithm applying similar conditions or parameters of wireless sensor network. The firefly algorithm is providing 94.46% efficiency of coverage in designing the layout of WSN while particle swarm optimization is providing 88.75%.

## Slide 52: Comparsion
Both experiment results
Experiments | PSO(best result) | Firefly(best result)
Experiment 1 | 94.46% | 97%
Experiment 2 | 88.75% | 91.6%

## Slide 53: Multi Objective Firefly Algorithm simulation and results
The simulation is conducted on the basis that how MOFA will provide positive results to solve multi-objective problem of wireless sensor network
Experiment setup :
The wireless sensor network is simulated with following parameter: grid size of 10X10 , 10 sensors , communication radius of 2m and HECN is placed at the center.
Multi-objective firefly algorithm is implemented to solve this problem while providing the user with Pareto optimal points